Note: This process has the site survey on it and I would not recommend a customer to try and use it.

Unzip the files and maintain the directory structure. These files are to be loaded on a PC that will work in the Janus.

If your PC does not support Type 1 PC cards you may have to load the files onto the PC card in the Janus.

Connect the JANUS device to a host PC(Null Modem Cable) and using Interlnk/Intersvr, copy all of the files to the PC card in the Janus(maintain the directory structure). Using Dos command xcopy or copy should work to copy the files over. 
Note: You need to perform either of these options prior to setting up the Security ID on the JANUS device. You can only see one section of a PC-size screen on the smaller display of a JG2010/JG2020. Use the viewporting feature to move around the screen.

To start the utility:

1. Boot the Janus unit and go to a Dos prompt.
2. Change directory to the PC card (F:\ or G:\).

3. Type in SS.bat(E model radio), SS1.bat(A->D model radio).
4. Tab to the Test/Utilities Menu.

5. Press “Enter”

6. Tab to the Security ID menu.

7. Press “Enter”

8. A warning message about the security ID option appears, 
   "Warning: AccessNet cards communicate only with other AccessNet cards with the same Security ID. Be sure to set the Security ID on all AccessNet cards in the same subnetwork to the same value."
 9. Press "Enter" to continue.
10.Type in your security ID(you can use up to 20 alphanumeric characters) and then “OK” it.

Note: The security ID you are entering is case-sensitive, if you want to delete the security ID if you no longer want to use this feature. Just delete all the character and press "Enter".

11. Next a message will inform you that your security ID has been updated.

Your AccessNet security ID has been updated.
  Press "Enter" to continue and a message will inform you of the JANUS device node address.

Note: If you are not within range of an access point with the security ID set, you can ignore the message that the JANUS device could not find a Master to synchronize with. 
  However, if you are within range of an access point and the security ID is correct, the message box informs you that the JANUS device is synchronized to the access point and provides the node address of the access point.
12. Exit out of menus and this should set the security ID.
13. Reboot the unit (ctl, alt, del).